# Reference
## Macros
### WG_LCLFUNCTION(name, ...)
### WG_LCLFUNCTION_TPL(name, ...)
### WG_LCLFUNCTION_END
    These macros start and end local function definitions and, as such, must be used within a declarative context. Their syntax is defined here. WG_LCLFUNCTION is for use in non-template functions and WG_LCLFUNCTION_TPL is for use in template functions; and both accept the following named parameters:
2. return
  Used to specify the return type of the local function. If not used, the return type defaults to void.
3. params
  Used to specify the signature of the local function. If not used, the signature defaults to void.
  The number of arguments for this named parameter is limited by WG_PP_LCLFUNCTION_CONFIG_PARAMS_MAX_ARITY.
4. varbind
  Used to bind function variables with variables of the same name in enclosing scopes. For more information see Bound Function Variables.
5. varset
  Used to set function variables with user declared expressions. For more information see Set Function Variables.
### WG_LCLFUNCTION_TYPE(name)
Expands to the implementation defined type name of the local function named name.
### WG_PP_LCLFUNCTION_CONFIG_PARAMS_MAX_ARITY
A user configurable object macro that controls the maximum number of arguments that may be specified for the named parameter params. If set, then it must expand to a non-negative integer, else it defaults to the number 15.
The maximum number of arguments which params can handle is equal to:
min( WG_PP_LCLFUNCTION_CONFIG_PARAMS_MAX_ARITY, BOOST_PP_LIMIT_REPEAT )
## Function Variables
Function variables are variables that are associated with each local function. They can be accessed directly from within the local function body and preserve their state across multiple calls to the same local function instance. There are two types of function variables: bound and set, and each are described below.
Note: Function variables are not necessarily implemented as member variables of a function instance. It is an implementation detail what form they take. That's why they're specified with var prefixed names and not mem prefixed names.
Note: It is the user's responsibility to ensure that at the time of a local function invocation all its function variables are valid. (See limitations for more information.)
### Bound Function Variables
Bound function variables are specified using the named parameter varbind. They are so named because their values are bound to variables of the same name from the enclosing scope(s).
#### this_
Bound variables named this_ are implicitly bound to this keyword, this is in keeping with existing BOOST conventions. If implicitly typed and explicitly qualified const then the constness will apply to the pointed-to-type and not the type of this_ (see Rationale).
### Set Function Variables
Set function variables are specified using the named parameter varset. They are so named because their values are determined by user specified expressions. Such an expression may contain identifiers from the enclosing scope(s), but not any declared in varset itself. If the said expression contains any commas, then the whole expression must be wrapped in an extra set of parenthesis (see Limitations). Additionally, neither shall it be an array initializer if compiling for C++03 (see Limitations).
### Explicit vs Implicit Types
Function variables may be explicitly or implicitly typed. If implicitly typed, the types of such variables are determined from the variable they are bound to, or, from the expression they are set to, via BOOST_TYPEOF. Thus, it is important to remember that implicitly typed variables lose their top-most const or reference qualification (see BOOST_TYPEOF).
#### Explicit Type Specification Syntax
Function variables are explicitly typed when their declarations are preceded by type(type-specifier), where type-specifier is defined in the C++ standard and the actual type of the associated function variable must be implicitly convertible to it.
#### Implicit Type Specification Syntax
Function variables that are not explicitly typed are implicitly typed. Their declaration may be preceded by the keyword combinations const, ref, or const ref, indicating how their deduced types should be top-most qualified. Hence, an implicitly typed function variable shall not be named "ref".
## Standard Type Names and Constants
### Local Function Type Name
The type of any local function object may be obtained from WG_LCLFUNCTION_TYPE.
### Local Function Typedefs and Constants
Each local function defines the following typedefs and constants:
- static std::size_t const arity
- result_type
- arg1_type
- ...
- argN_type
Where result_type is an alias for the return type of the local function, and argM_type is an alias for the Mth element of boost::function_type::parameter_type<local-function-signature>. These are analogous to the type names and constants defined by boost::function_traits in Boost.TypeTraits library.
Note: from within the local function body the above can be directly accessed. Outside the local function body one must use the local function type name scope to access them.
## Interactions with Boost.Function
Local functions may be assigned to Boost.Function's boost::function, and, respecting all the usual caveats, returned from their scope of definition.
Note: the const qualification of a boost::function wrapped local function will not affect how the local function is called, it only affects whether the boost::function object can be mutated or not.
## Interactions with other LclFunctions
### As Function Variables and Function Parameter Arguments
Because local functions have non-local types, they may be used as arguments to local function variables and local function parameters.
### Nesting
Local functions may be nested within one another and may even reuse the same name, with the inner most scope name overriding all others.
### Same Line Declarations
Multiple local functions may be declared on the same line, for example, as part of a larger macro definition.
# Limitations
## C++03 Limitations
### Library Boundaries
Local functions may not be usable across library boundaries because their user-provided definitions are ultimately implemented using local types, and in C++03 local types lack linkage. Hence, their symbols may not have been exported.
### Set-To Expressions
In C++03 the set-to expressions of a set function variable shall not be array initializer. This is because array initializers may not be used as parameter arguments in C++03. This restriction may be relaxed but the work around was deemed not worth the effort, especially given the existence of better alternative data types such as std::vector and boost::array.
## General Limitations
### Macro Parameters Containing Commas
The preprocessor treats commas appearing within macro parameters as delimiters; hence they are to be avoided in type expressions and wrapped with an extra set of parenthesis when used with value expressions. The former is necessary because there is no known way to extract user specified type in C++03. (The lack of variadic macros prevents us from using PPMP tools and any known TMP tool will ultimately loose the top-most const qualification from any such expression.) The latter is necessary to prevent the comma from acting as a delimiter in the preprocessor and, hence, making it appear as if the function-like macro had extra parameter(s).
### Local Function Variables
Local function variables must be valid at the time of any invocation of their associated local function instance. This means that if any local function variable references any non-local function object, that object must be valid at the time of the associated local function invocation.
### Local Function Definitions
Local functions are ultimately implemented using local class functions, hence any limitations imposed by the language on the latter will also carry over to the former.
# Grammar
## Special Symbols
1. [...]
  Items enclosed in square brackets denote optional grammar entries.
2. return params type varbind varset const ref
  These tokens are to be regarded as non-punctuation terminals.
## EBNF

lclfunction-usage ::=
  lclfunction-start-macro ( name , lclfunction-spec )
  function-body
  WG_LCLFUNCTION_END [;]

lclfunction-start-macro ::=
    WG_LCLFUNCTION
  | WG_LCLFUNCTION_TPL

lclfunction-spec ::=
    void
  | [return nlt-return-tuple]
    [params param-seq]
    [varbind varbind-seq]
    [varset varset-seq]

nlt-return-tuple ::=
    ( non-local-type )

param-seq ::=
varbind-seq ::= nlt-bound-tuple-seq
varset-seq ::= nlt-set-tuple-seq

nlt-bound-tuple-seq ::=
    nlt-bound-tuple
  | nlt-bound-tuple-seq nlt-bound-tuple

nlt-set-tuple-seq ::=
    nlt-set-tuple
  | nlt-set-tuple-seq nlt-set-tuple

nlt-bound-tuple ::=
  ( nlt-bound-var-dcln )

nlt-set-tuple ::=
  ( nlt-set-var-dcln )

nlt-bound-var-dcln ::= nlt-type-var-dcln

nlt-set-var-dcln ::= nlt-type-var-dcln , value-expr

nlt-type-var-dcln ::=
    implicit-non-local-type-var-dcln
  | explicit-non-local-type-var-dcln

implicit-non-local-type-var-dcln ::=
  implicit-type-var-dcln

explicit-non-local-type-var-dcln ::=
  explicit-non-local-type var-name

implicit-type-var-dcln ::=
  implicit-type var-name

implicit-type ::= lib-type-qualifiers | empty-string

lib-type-qualifiers ::= const | ref | const ref

explicit-non-local-type ::=
    type( non-local-type-specifier )

function-body ::= See C++ standard.
var-name ::= A C++ variable name.
non-local-type-specifier ::=
  A type-specifier that specifies a non-local type.
type-specifier ::= See C++ standard.
value-expr ::= A C++ expression evaluating to some value.

# Design Rationale
## Preprocessor Limitations
### Multi-Input User Specification
Depending on preprocessor support, multi-input specification may take the form of a single n-tuple, or a sequence of n 1-tuples, where the former is allowed only if variadic macros are supported by the preprocessor. The reasoning for this is that an n-tuple is easier to read and type than a sequence of n 1-tuples. For example:
params (int x, int y, std::string label)
is assumed to be preferable to:
params (int x) (int y) (std::string label)
## params Named Parameter Specification Format
The specification for the named parameter params needs to be PP parseable because the codegen needs to construct an expanded parameter list from those entries. That is, we need to be able to insert a comma before and after the full list of those entries. As a result, if variadic macros are not supported then params must be specified as a sequence of 1-tuples.
## Forwarding Strategies of params Arguments
Any code generated for WG_PP_LCLFUNCTION must involve a two step function call where an external function forwards any of the arguments of "params" to an internal function that encapsulates the user defined scope of this macro. The reason for this is to get around the C++03 rule of local classes not being usable in template parameters. In this section we discuss the forwarding strategy used, an alternative using the existing syntax, and other alternatives using slightly different syntax for param-tuple arguments of params.
For the rest of this this discussion will use variants of the following example:
WG_PP_LCLFUNCTION(func, params (...) )
which, without loss of generality, we can assume will generate the following code:
void interface_func(...);
void impl_func(...);
where interface_func is the external function that merely forwards all of its parameters to impl_func. It is important to note that:
1. in the generation of interface_func only TMP tools are available for use, and
2. in the generation of impl_func both PPMP and TMP tools are available for use.
Additionally, we don't have much leeway in generating interface_func because its signature and return type must be semantically equivalent to the one specified by WG_PP_LCLFUNCTION macro; this is because, as its name implies, interface_func is the client facing interface to the user specified and defined local function. (If this were not the case, then dispatching interface_func based on its signature in TMP code may result in surprising and unexpected behavior.)
### Current Forwarding Strategy
The current forwarding strategy for the current syntax of params is best illustrated using the following example:
WG_PP_LCLFUNCTION(func, params (big_type const x) )
will generate:
void interface_func(big_type x);
void impl_func(big_type const x);
where the body of interface_func just calls impl_func(x)
The rationale for interface_func's signature are:
1. Because the token "big_type const x" is not PP parseable, only TMP techniques are left to deduce its type. And the only relevant tool available is function_types::parameter_types, where the latter can and/or does strip off the top most const qualifier. (Remember, BOOST_TYPEOF is by default not used unless explicitly specified by the user, and in this case is certainly not needed.) Thus, the top-most const qualification of any specified local function parameter argument type is subject to being lost.
2. C++ semantic equivalency with the signature specified by the user. Even though the top-most const qualification of any parameter argument type maybe stripped off for interface_func, its signature and the users specified signature are still equivalent under C++ rules.
The rationale for impl_func's signature is:
1. simplicity.
2. codegen limitations. Since the token "big_type const x" is not PP parseable, there is no way to correctly optimize it's forwarding in the said signature. This is because TMP tools will have to be used to deduce the type of the token, and any such use will result in the top most const qualifier being lost. Which in the context of impl_func's user defined scope will result in an incorrectly typed parameter potentially being used. (That is x's compiler enforced immutability should not be lost in the user defined local function scope.)
3. compiler optimizations. It is assumed the compiler will optimize away the extra copy at impl_func's call site in interface_func's definition since the latter's code just literally consists of forwarding parameter arguments to the former.
### Alternative Forwarding Strategy with Alternative param-tuple Syntax
It is possible to efficiently forward interface_func's parameter arguments to impl_func if the former's parameter types were exactly deducible. To this end we could modify the param-tuple syntax to delimit the parameter type from the parameter name along the lines of the following:
WG_PP_LCLFUNCTION(func, params (type(big_type const) x) )
This will allow us to generate:
void interface_func(big_type const x);
void impl_func(big_type const & x);
which correctly and efficiently forwards interface_func's parameter arguments to impl_func. (This is possible because during the preprocessing phase we are able to parse the exact type of x and, hence, manipulate it accordingly when generating code.)
This syntax was considered and implemented at one point but was considered too unwieldy and not worth the unproven benefits of efficient forwarding.
## this_ const Qualified Bound Function Variables
The const qualification of this_ bound function variables applies to the pointed-to-type of this_ because its type, and hence the type of this, are already const qualified. Not only would it be redundant, but it would also be impossible to const qualify the pointed-to-type of an implicitly typed this_ had the constness been applied to the pointer type.
# Future Features
## function_type
A typedef aliasing the local function's specified signature and return type.
## make_ref/make_cref
Creates a reference wrapper for local function objects for use with STL algorithms were the user wants to ensure reference semantics for any and all copies.